FIRST INTERNATIONAL COMPUTER
7F., Yang Kuan Street, Neihu,
114 Taipei, Taiwan R.O.C.

HARDWARE SPECIFICATIONS FOR NEO 1973 GTA01BV4
Physical Dimensions
- 120.7 x 62 x 18.5 mm (4.75 x 2.44 x 0.728 inch)
- 184 +/- 5 g (6.5 ounces)
Main components
Processor
Samsung S3C2410AL-26 (Capable of running up to 266 MHz)
Flash
64MB Samsung NAND flash (K9F1208U0B) attached to S3C2410 NAND controller.
RAM
128MB SDRAM (2x Samsung K4M511633C) attached to S3C2410 SDRAM controller
GSM/GPRS
The GSM (including GPRS) modem is Texas Instruments Calypso based.
CALYPSO digital baseband
TWL3014 analog baseband
TRF6151 RF Transceiver

Quad-band support (850/900/1800/1900)
GPRS Class12/CS4
AGPS
Hammerhead PMB 2520 AGPS from Global Locate.
Externally-accessible GPS antenna connector of type MMCX
microSD-Card
The Neo1973 has one microSD aka. Transflash slot. It should support SDHC, but this has not been tested. If this works, cards >2G should work with no problems. As there are no microSD cards over 2G at the moment, it hasn't been tested. MicroSD slot is under battery.
LCD Module (LCM)
This is a 2.8" diagonal (1.7" x 2.27" - 43mm x 58mm) 480x640 toppoly (tpo) TD028TTEC1 module, using a Toshiba JBT6K74 TFT LCD Driver Chipset.
Touch Screen
Stylus
Bluetooth
Delta DFBM-CS320 Class2 Module, using CSR BlueCore4
Vibrator
USB Host
USB Device
The USB Device controller is inside the S3C2410
Audio
Wolfson Codec
There's a WM8753 Wolfson Microelectronics CODEC (This is not a 'smart' codec that can interpret MP3/... it is a simple dumb 'sound card'.
Stereo Amplifier
There's a National Semiconductor LM4857 Stereo Amplifier at the analog audio output of the WM8753
Analog wired Headset
There's a four-ring 2.5mm stereo jack which provides connectivity to old-fashioned wired headsets.
The headsets used by Motorola smartphones (A780,A1200, ...) and the V-360 have a compatible configuration.
Bluetooth Headset
This one is wired via PCM bus from the CSR Bluetooth chip to the Wolfson codec.
Power Management
A Philips PCF50606 is used for power management.
Battery
The Neo1973 Battery is compatible with a Nokia BL5C battery.
Buttons
The Neo1973 features two buttons:
1. The Power Button
2. The "Aux" button
Approval
- CE
- FCC